## Slide 1: Multispectral Optoacoustic Tomography
Kyle Jones

## Slide 2: Background
Multispectral Optoacoustic Tomography (MSOT): a non-invasive molecular imaging method that can be used to diagnose tumors and monitor treatment response.
  MSOT spectra contain information relevant to clinicians, such as tumor oxygenation and vascular perfusion
MSOT spectra are currently evaluated using a spectral unmixing technique that works well under noise-free conditions, but poorly under noisy conditions.
  Machine learning algorithms may perform better under noisy conditions.

## Slide 3: Purpose
Purpose 1: compare the accuracy and precision of Hemoglobin (Hb), Oxygen (O2) and ICG fractional component measurements between the traditional spectral unmixing method and machine learning methods.
  Comparisons will be done under noise-free and noisy conditions.
Purpose 2: determine the optimal wavelength components when acquiring an MSOT spectrum
  Under in vivo conditions, it’s not realistic to acquire densely sampled spectra
  If we only have time to acquire 6 images (i.e., 6 wavelengths), what wavelengths will give the most accurate Hb, O2, and ICG measurements?
  Do machine learning methods work better than the traditional unmixing method when the MSOT spectrum is sparse?

## Slide 4: What has been done so far?

## Slide 5: Coded the traditional unmixing method in Python
Y (experimental MSOT signal) | Hb (known 100% Hb spectrum) | O2 (known 100% O2 spectrum) | ICG (known 100% ICG spectrum)
1 | 1 | 1 | 1
0.8 | 0.9 | 0.7 | 0.5
0.72 | 0.8 | 0.5 | 0.1
Dataset
1 | 1 | 1 | 1
…
n
experimental MSOT signal at n wavelengths
known 100% Hb MSOT signal at n wavelengths
known 100% O2 MSOT signal at n wavelengths
known 100% ICG MSOT signal at n wavelengths
Spectral Unmixing Method
Y = B1 x Hb + B2 x O2 + B3 x ICG
estimated Hb fraction in Y
estimated O2 fraction in Y
estimated ICG fraction in Y
estimate B1, B2, and B3 using linear regression with nonnegative least squares, to ensure you don’t get negative fractional components.

## Slide 6: Developed machine learning alternative
Y1 (Hb fraction) | Y2 (O2 fraction) | Y3 (ICG fraction) | X1 | X2
1 | 0 | 0 | 0.38 | 0.67
0.9 | 0.1 | 0 | 0.22 | 0.89
0.8 | 0.2 | 0 | 0.01 | 0.96
0.7 | 0.3 | 0 | 0.57 | 0.37
0.6 | 0.4 | 0 | 0.82 | 0.85
0.5 | 0.5 | 0 | 0.86 | 0.93
Dataset
…
Xp
0.45
1.00
0.47
0.66
0.28
0.93
0 | 0 | 1 | 0.34 | 0.29
0.16
…
p wavelengths, where each wavelength is a predictor.
X
y
n
number of data points
There are machine learning algorithms that support multioutput predictions (e.g., linear regression, k-nearest neighbor, decision tree, etc.).
https://machinelearningmastery.com/multi-output-regression-models-with-python

## Slide 7: Developed data collection plan
Acquire high SNR MSOT spectra at 1 mm wavelength steps between 680 nm to 900 nm.
X MSOT spectra will be collected at X different mixtures of Hb, O2, and ICG.
Data will be collected by X

## Slide 8: Plans after data is collected?

## Slide 9: Machine learning vs. traditional method

## Slide 10: Optimal wavelengths to collect