## Slide 1: Multispectral Optoacoustic Tomography
Kyle Jones

## Slide 2: Background
Multispectral Optoacoustic Tomography (MSOT): a non-invasive molecular imaging method that can be used to diagnose tumors and monitor treatment response.
  MSOT spectra contain information relevant to clinicians, such as tumor oxygenation and vascular perfusion
MSOT spectra are currently evaluated using a spectral unmixing technique that works well under noise-free conditions, but poorly under noisy conditions.
  Machine learning algorithms may perform better under noisy conditions.

## Slide 3: Purpose
Purpose 1: compare the accuracy and precision of Hemoglobin (Hb), Oxygen (O2) and ICG fractional component measurements between the traditional spectral unmixing method and machine learning methods.
  Comparisons will be done under noise-free and noisy conditions.
Purpose 2: determine the optimal frequency components when acquiring an MSOT spectrum
  Under in vivo conditions, it’s not realistic to acquire densely sampled spectra
  If we only have time to acquire 6 images (i.e., 6 frequencies), what frequencies will give the most accurate Hb, O2, and ICG measurements?
  Do machine learning methods work better than the traditional unmixing method when the MSOT spectrum is sparse?

## Slide 4: What has been done so far?

## Slide 5: Coded the traditional unmixing method in Python
Y (experimental MSOT signal) | Hb (known 100% Hb spectrum) | O2 (known 100% O2 spectrum) | ICG (known 100% ICG spectrum)
1 | 1 | 1 | 1
0.8 | 0.9 | 0.7 | 0.5
0.72 | 0.8 | 0.5 | 0.1
Dataset
1 | 1 | 1 | 1
…
n
experimental MSOT signal at n frequencies
known 100% Hb MSOT signal at n frequencies
known 100% O2 MSOT signal at n frequencies
known 100% ICG MSOT signal at n frequencies
Spectral Unmixing Method
Y = B1 x Hb + B2 x O2 + B3 x ICG
estimated Hb fraction in Y
estimated O2 fraction in Y
estimated ICG fraction in Y
estimate B1, B2, and B3 using linear regression with nonnegative least squares, to ensure you don’t get negative fractional components.

## Slide 6: Studied possible machine learning alternative
Y1 (Hb fraction) | Y2 (O2 fraction) | Y3 (ICG fraction) | X1 | X2
1 | 0 | 0 |  | 
0.9 | 0.1 | 0 |  | 
0.8 | 0.2 | 0 |  | 
0.7 | 0.3 | 0 |  | 
0.6 | 0.4 | 0 |  | 
0.5 | 0.5 | 0 |  | 
Dataset
…
Xn
1 | 1 | 1 | 1 |